## Slide 1: FORCE MODELING FOR OBLIQUE CUTTING ON NON-PLANAR SURFACES
Dual degree project review meeting
19-10-2016
Department of Mechanical Engineering
Submitted By: Ayush Bandil Guide: Prof. Anirban Guha & Prof. Asim Tewari

## Slide 2
Ref: http://images.fineartamerica.com/images-medium-large/tray-table-on-an-airplane-jaak-nilson.jpg

## Slide 3: INTRODUCTION
Extremely tight tolerance limit is required in Industries like aerospace and automotive
Limitations of conventional 3-axis milling processes:
  Tolerance limit: High forces
  Tool wear: Quality
  Tool accessibility: free form surfaces
Lead and tilt

## Slide 4
Feed
Normal
Cross feed
lead
tilt

## Slide 5: PROJECT OBJECTIVE AND MOTIVATION
Motivation:
Analytical empirical and numerical models exist for
Limited geometries: mainly ball-end
Workpiece material: Titanium alloy Ti6Al4V
Planer geometries: not edges and corners
Overall aim: To develop a general methodology to predict the cutting forces during the 5-axis milling process
Phase 1 objective: Model for ball end cutting tool with helical cutting edge operating on planer geometries in one direction

## Slide 6
LITERATURE REVIEW

## Slide 7
Many researchers have worked on milling processes across the world:
P. Lee and Y. Altintas, 1995, “PREDICTION OF BALL-END MILLING FORCES FROM ORTHOGONAL CUTTING DATA”: Basic analytical model with helical ball-end mills
L. Xu , J. K. Schueller & J. Tlusty, 1998, “A simplified solution for the depth of cut in multi-path ball end milling”: Path increment angle in 3-axis milling which is analogous to the tilt angle
Lazoglu, Koc university, Turkey in 2003: completely experimental on boring process
E. Ozturk and E. Budak, 2007, Istanbul, Turkey published “MODELING OF 5-AXIS MILLING PROCESSES”: dealt with complete
Binglin Li , Yujin Hu, Chenggang Li & Xingxing Li, China, 2011 “AN ANALYTICAL MODEL OF OBLIQUE CUTTING WITH APPLICATION TO END MILLING”: conversion of orthogonal cutting parameters to oblique cutting

## Slide 8: GEOMETRICAL MODELLING OF BALL-END MILL
Step 1
Establishing coordinate systems for cutting tool as well as workpiece
Mathematical formulation of tool geometry
Step 3
Defining cutting edge parameters
Step 4
Discretization of surface and
Step 5
Identification of engagement region (cutting zone)
Step 6
Step 2
Step 7
Step 8
Computation of elemental forces and torques
Transformation of forces and torques to TCS and then FCN
Determining chip dimensions
Determining edge and cutting force coefficients
Step 9

## Slide 9
Feed
z
Cross feed
Normal
x
y
radial
tangential
axial

## Slide 10
Ref: http://www.sgstool.com/images-dev/_products/series-1b.jpg

## Slide 11: STEP 2 & 3: TOOL AND CUTTING EDGE GEOMETRIC PARAMETERS
  Tool Geometry: 𝑥2+𝑦2+(𝑅0−𝑧)2=𝑅02
  Flutes or cutting edge: helix angle i0
  Cutting edge parameters:
  Distance from tool tip along tool-axis (Z)
  Local radius r(z)
  Axial immersion angle
  Lag angle Ψ: angle on x-y plane in TCS between the line which connects the cutting point to the tool tip
  Radial Immersion angle
Helical cutting edges on ball end mill envelope

## Slide 12: STEP 2 & 3: TOOL AND CUTTING EDGE GEOMETRIC PARAMETERS
Helical cutting edges on ball end mill envelope
r(z)

## Slide 13
  In Tool Coordinate System:
  𝑥𝑥𝑡𝑐𝑠(𝑧) = 𝑟(𝑧) ∗ sin𝛷(𝑧)
  𝑦𝑦𝑡𝑐𝑠(𝑧) = 𝑟(𝑧) ∗ cos𝛷(z)
  𝑧𝑧𝑡𝑐𝑠(𝑧) = 𝑧
Angular incremental (𝑑𝜃) and axial incremental (𝑑𝑧) values: to control the density
  Number of angular integration points (𝐾𝑝)
  𝐾𝑝 =
  Axial integration points (𝐿𝑝)
  𝐿𝑝 =
Discretized points in FCN coordinate system envelope
STEP 4: DISCRETIZATION OF SURFACE

## Slide 14: STEP 5: IDENTIFICATION OF CUTTING ZONE
Discretized points in FCN coordinate system envelope

## Slide 15: STEP 5: IDENTIFICATION OF CUTTING ZONE
  Identified by removing two sets of points from the set of cutting points:
  Points above the cutting depth
  Points lying opposite to the direction of the feed in FCN coordinate system
  Logical Matrix (LG)
Discretized points in FCN coordinate system envelope
Top view of discretized points below the cutting depth
for 200 lead 300 tilt
Top view of discretized points in the cutting zone
for 200 lead 300 tilt

## Slide 16: STEP 6: CHIP DIMESIONS
The forces generated depend on the geometry on the chips formed.
There are three geometric parameters which are as follows:
  Chip thickness:
  Chip width: projected length of an element in the direction of cutting velocity:
  Chip length: distance between two adjacent cutting points:

## Slide 17: STEP 7: EDGE AND CUTTING FORCE COEFFICIENTS
EDGE FORCES
Rubbing of the tool against the workpiece material
For Ti6Al4V, finding a regression model using experimental results
The coefficients are defined force per unit length
Ref: E. Budak and E. Ozturk, "Modeling of 5-axis Milling Processes
CUTTING FORCES
Shearing of the workpiece material in the shear zone
Coefficients are defined forces per unit chip area.

## Slide 18: STEP 8: ELEMENTAL FORCES AND TORQUE
Total forces on any cutting element is the vector sum of cutting and shear force. The elemental tangential, radial and radial force acting on the cutting edge are expressed as:
Where,
Logical matrix is multiplied by chip dimensions to nullify the effect of points not lying the cutting zone and only consider the points lying in the cutting zone.

## Slide 19: STEP 9: FORCE CALCULATION IN TCS and FCN
Where,
Elemental Torque:

## Slide 20: STEP 9: FORCE CALCULATION IN TCS and FCN
The total cutting force in Tool Coordinate System:
Total torque:
The cutting forces are transformed into FCN coordinate system
Where,

## Slide 21
RESULTS AND VALIDATION

## Slide 22: CASE 1: Inputs parameters: Diameter, D = 19.05mm Helix angle, i0 = 300 Rake angle, = 00 Number of flukes, Nf = 1 Spindle speed, n=269 rpm Table feed, St = 13.6652 mm/min Depth of cut = 6.35mm Lead angle = 00 Tilt angle = 00
1 cutting edge
Variation of F, C and N forces with rotational angle
As the cutting edge starts coming out of the cutting region all the three components start tending to zero.
Ref: P. Lee and Y. Altintas, “Prediction of ball end milling forces of orthogonal cutting data”

## Slide 23: CASE 1: Inputs parameters: Diameter, D = 19.05mm Helix angle, i0 = 300 Rake angle, = 00 Number of flukes, Nf = 1 Spindle speed, n=269 rpm Table feed, St = 13.6652 mm/min Depth of cut = 6.35mm Lead angle = 00 Tilt angle = 00
In this case, the ball-end tool has only 1 cutting edge.
Variation of F C and N forces with rotational angle
As the cutting edge starts coming out of the cutting region all the three components start tending to zero.

## Slide 24: CASE 2: Inputs parameters: Diameter, D = 19.05mm Helix angle, i0 = 300 Rake angle, = 00 Number of flukes, Nf = 2 Spindle speed, n=500 rpm Table feed, St = 100 mm/min Depth of cut = 6.35mm Lead angle = 300 Tilt angle = 300
lead and tilt angels are not zero, i.e. one of the cutting edge is already in the cutting zone and hence forces and torque do not start from zero.
Ref: E. Ozturk and E. Budak, “Modeling of 5-axis milling Processes, machining science and Technology”

## Slide 25: CASE 3: Inputs parameters: Diameter, D = 20mm Helix angle, i0 = 300 Rake angle, = 00 Number of flukes, Nf = 3 Spindle speed, n=500 rpm Table feed, St = 100 mm/min Depth of cut = 10mm Lead angle = 200 Tilt angle = 100
Tool profiles and cutting zone

## Slide 26: CASE 3: Inputs parameters: Diameter, D = 20mm Helix angle, i0 = 300 Rake angle, = 00 Number of flukes, Nf = 3 Spindle speed, n=500 rpm Table feed, St = 100 mm/min Depth of cut = 10mm Lead angle = 200 Tilt angle = 100
Reason for abrupt plot

## Slide 27: Determining Lead and Tilt Angles
Depth of cut = 2.5mm
Lead and tilt angles for minimum force on
the cutting tool are -200 and 40 respectively.
Depth of cut = 5mm
Lead and tilt angles for minimum force on
the cutting tool are -340 and 80 respectively.
As we increase the depth of cut, the lead and tilt angles also need to be increased (magnitude) to get the minimum value of Fxy_max

## Slide 28: SHORTCOMINGS OF THE CURRENT MODEL
Calculation of chip dimensions do not consider the effect of rotation of the tool.
The axial discretization is based on taking constant values of axial increment which results in unequal chip widths. For a cutting element chip width is defined as
For angles, which are close to zero degree, the chip width is very large and hence inaccurate.
The current model is developed only for ball-end milling tool are not valid for other tool shapes.
The workpiece is considered to be planer and the tool is performing a straight slot milling operations.

## Slide 29: CONCLUSION AND PLAN FOR PHASE II
http://www.wilmotyeh.com/me/images/fullsize/IMG_9706a.JPG

## Slide 30: CONCLUSION AND PLAN FOR PHASE II
The simulated results are consistent with the results in published literature. The lead and the tilt angles for the minimization of the cutting forces are predicted using the model.
The model can also be used to predict other machining parameters for the optimization of the cutting process such as precision, cutting depth, feed rate and time required to finish the job.
Future aspects of the project are as follows:
Extension of the model from flat workpiece surface to edge and corner surfaces. Results can be achieved for both types of edge surfaces (Inner and outer edge surfaces) and corner surfaces (inner, outer and combination of both).
Extension of the model to incorporate other tool geometries.
Experimental validation of the data. Current model has been benchmarked against published literature data.
Development of Orthogonal Cutting Data (OCD) for other materials based on experimental results

## Slide 31: REFERENCES
1) E. Ozturk, T. Tunc and E. Budak, "INVESTIGATION OF LEAD AND TILT ANGLES EFFECT IN 5-AXIBALL-END MILLING PROCESSES," International journal of machine tools and manufacture, pp. 1053-1062, 2009.
2) E. Budak and E. Ozturk, "Modeling of 5-axis Milling Processes" 2007.
3) P. Budak and Y. Altintas, "Prediction of Milling Force Coefficients From Orthogonal Cutting Data," Department of Mechanical Engineering, The University of British Columbia, Canada.
4) P. Lee and Y. Altintas, , "PREDICTION OF BALL END MILLING FORCES FROM ORTHOGONAL CUTTING DATA," International journal of machine tools and manufacture, pp. 1059-1072, 1996.
5) B. Li, H. Yujin, X. Wang and C. Li, "AN ANALYTICAL MODEL OF OBLIQUE CUTTING WITH APPLICATION TO END MILLING," Machining Science and Technology, An International Journal, pp. 453-484, 2011.
6) Y. ALTINTAS, "METAL CUTTING MECHANICS, MACHINE TOOL VIBRATIONS, AND CNC DESIGN," in MANUFACTURING AUTOMATION Second edition, p. Chapter 2.

## Slide 32
THANK YOU